## Slide 1: Embedded Linux
Configuration & Build Process of an Embedded Linux System
Notes: Hello and welcome to the Linux for Embedded Systems lecture. This is the fourth lecture of the course.

## Slide 2: Goal
To illustrate the configuration & build process of an embedded Linux system
To illustrate the concept of build systems
Notes: The aim of this lecture is to
  - Illustrate the configuration and build process of an embedded Linux system.
  - Illustrate the concept of build systems.

## Slide 3: Summary
Introduction
The Workflow
The Build Systems
Yocto
Notes: We will begin with a quick overview of what an embedded Linux system requires to operate.

## Slide 4: Summary
Introduction
The Workflow
The Build Systems
Yocto
Notes: We will begin with a quick overview of what an embedded Linux system requires to operate.

## Slide 5: Introduction
An embedded Linux system requires the following components to operate:
  The Bootloader
  The Linux Kernel
  The Device Tree Blob (DTB)
  The Root File System
All these components must be:
  Configured for the embedded system hardware platform
  Compiled and linked into an executable format
  Deployed into the embedded system persistent storage for booting and operations
U-Boot
Linux Kernel
DTB
Root File System
MicroSD card image layout
RAW unformatted space
FAT file system
Linux-native file system
Photo by Jeremy Singer
Notes: An embedded Linux system requires the following components in order to operate properly:
  A bootloader
  A Linux kernel
  A device tree blob
  A root file system
These components must be:
  Configured for the embedded system hardware platform.
  Compiled and linked into an executable format.
  Deployed into the embedded system persistent storage for booting and operations.
The board’s U-Boot partition is RAW unformatted space.
The kernel and Device Tree Blob are part of a FAT file system.
The root file system is part of a Linux-native file system, typically ext4.

## Slide 6: Summary
Introduction
The Workflow
The Build Systems
Yocto
Notes: We will now look at the workflow of an embedded system.

## Slide 7: The Workflow
Bootloader source code
Linux Kernel
source code
Hw-specific configuration
Cross compiler
Hw-specific configuration
Cross compiler
System programs source code
Application specific configuration
Cross compiler
Bootloader binary
Linux Kernel
binary
DTB
Root File System
System programs binary
Notes: This diagram illustrates the process to configure the specific components. We will take a more in-depth look into each of these.

## Slide 8: The Workflow
The Bootloader source code shall be procured.
It shall be configured for the specific hw of the embedded system.
  The proper CPU shall be selected.
  The proper board shall be selected.
  Custom configuration may be needed if the hw is non-standard.
It shall be cross-compiled for the CPU of choice obtaining the executable code.
It shall be copied into the boot device.
  First sector of a MicroSD card
  Bootflash device on the embedded system board
Bootloader source code
Hw-specific configuration
Cross compiler
Bootloader binary
Notes: To begin, the bootloader source code is obtained and configured for the specific hardware of the embedded system. For example, the correct CPU and board are selected, and some custom configuration may be required if the hardware is non-standard.
It is then cross-compiled for the CPU of choice, providing the executable code.
Then, it is copied onto the boot device, such as a sector of a microSD card or a boot flash device on the embedded system board.

## Slide 9: The Workflow
The Linux Kernel source code shall be procured.
It shall be configured for the specific hw of the embedded system.
  The proper CPU shall be selected.
  The proper board shall be selected.
  Custom configuration may be needed if the hw is non-standard.
It shall be cross-compiled for obtaining
  Executable Linux kernel
  Executable Linux kernel modules
  Device Tree Blob
The obtained files shall be copied into the boot device.
  Partition on a MicroSD device
  Bootflash device on the embedded system board
Linux Kernel
source code
Hw-specific configuration
Cross compiler
Linux Kernel
binary
DTB
Notes: The Linux kernel binary and Device Tree Blob are prepared in a manner very similar to the bootloader binary. The process begins with obtaining the kernel source code, which is then configured for the specific hardware of the embedded system. The correct CPU and board will be selected, and custom configurations may be made if the hardware is non-standard.
It is then cross-compiled and will produce an executable Linux kernel, executable Linux kernel modules, as well as a Device Tree Blob.
Once these are obtained, they can be put in a partition on a microSD card or onto a boot flash device on the embedded system board.

## Slide 10: The Workflow
The system programs source code shall be procured.
  Downloaded from Internet
  Received from operating system vendor
They shall be configured for the specific application.
  Only the system programs needed for the application the embedded system is intended for shall be considered.
They shall be cross-compiled obtaining the executable binary.
System programs source code
Application specific configuration
Cross compiler
System programs binary
Notes: The system programs source code can be obtained in a few different ways, either by downloading it from a source on the Internet or by receiving it from an operating system vendor.
They are then configured for a specific application. Only the system programs that are required for the application that the embedded system is intended for will be considered.
Next, they are cross-compiled, which provides the executable system program binaries.

## Slide 11: The Workflow
The root file system shall be prepared.
It typically requires
  To create a file and mount it as a volume on the development host
  To format it using any of the file systems Linux supports (e.g., ext3)
  To create the required directory tree
  To populate it with the needed configuration files
  To populate it with the system program binary
The root file system shall be copied into the embedded system persistent storage.
  Partition on a MicroSD device
  Bootflash device on the embedded system board
/ # Disk root
/bin # Repository for binary files
/lib # Repository for library files
/dev # Repository for device files
console c 5 1 # Console device file
null c 1 3 # Null device file
zero c 1 5 # All-zero device file
tty c 5 0 # Serial console device file
tty0 c 4 0 # Serial terminal device file
tty1 c 4 1 #
tty2 c 4 2 #
tty3 c 4 3 #
tty4 c 4 4 #
tty5 c 4 5 #
/etc # Repository for config files
inittab # The inittab
/init.d # Repository for init config files
rcS # The script run at sysinit
/proc # The /proc file system
/sbin # Repository for accessory binary files
/tmp # Repository for temporary files
/var # Repository for optional config files
/usr # Repository for user files
/sys # Repository for system service files
/media # Mount point for removable storage
Notes: The root file system is also prepared in the workflow. This process involves a number of things:
  - Creating a file and mounting it as a volume on the development host.
  - Formatting it using one of the file systems supported by Linux, for example ext3.
  - Creating the required directory tree.
  - Populating it with the needed configuration files.
  - Populating it with the system program binary.
The root file system is copied onto the embedded system’s persistent storage. This may be a microSD card or a boot flash device on the board itself.

## Slide 12: Summary
Introduction
The Workflow
The Build Systems
Yocto
Notes: We will now look at build systems.

## Slide 13: Build Systems
Building an embedded Linux system is a complex operation.
  Multiple sources shall be configured and compiled.
  Root file system shall be updated at each build through a non-trivial task.
  In cases of multiple hw and multiple hw configurations, manual iteration is needed.
Tools, known as build systems, are available to automate such operations.
Build systems takes care of:
  Building the cross compiler for the selected embedded system CPU
  Managing bootloader/kernel/system programs configuration
  Managing bootloader/kernel/system program build
  Preparation of the root file system and boot device image preparation
Notes: Building an embedded Linux system is a complex process for a few reasons. First, it requires the configuration and compilation of multiple sources with different dependencies. This can easily cause issues if the requirements are not fulfilled or if there is conflict between sources. The root file system is updated at each build, which is a non-trivial task. When it comes to the case of multiple hardware, as well as multiple hardware configurations, manual iteration is often required.
There are tools, known as build systems, which are readily available, that automate this process.
The build system manages building the cross compiler for the selected embedded system CPU and manages the bootloader, kernel and system program configuration, and build process. Finally, it also prepares the root file system and boot device image.

## Slide 14: Build Systems
Several solutions are available.
Hw-vendor custom-built systems
  NXP Linux Target Image Builder (LTIB)
Open-source build systems, among which the most popular are Yocto and Buildroot
  Very actively maintained and developed projects
  Widely used in the industry
  Built from scratch from source toolchain, bootloaders, kernel, and root file system
Notes: When it comes to build systems, there are several solutions available.
One option is for hardware vendors to custom build systems. These are designed for particular hardware. An example of this is the NXP Linux Target Image Builder.
Another option is to use one of the many open-source build systems, such as Yocto or Buildroot, which are among the most popular. These projects are typically actively developed and maintained, ensuring that they remain up-to-date. They are widely used across the industry.

## Slide 15: Buildroot vs Yocto: General Aspects
Buildroot
  Focus on simplicity
  Use existing technologies: kconfig, make
  Open community
Yocto
  Provides core recipes and use layers to get support for more packages and more machines
  Custom modifications should stay in a separate layer
  Versatile build system: tries to be as flexible as possible and to handle most use cases
  Open community but governed by the Yocto Project Advisory Board
Notes: Here is a brief comparison between Yocto and Buildroot in terms of their general workings.
Buildroot is focused on simplicity and uses existing technologies such as “kconfig” and “make”. It also benefits from an open community.
Yocto is slightly more complex. It provides the core recipes, but layers need to be included in order to get support for more packages or machines. Any custom modifications made should stay in a separate layer. Given this use of layers and recipes, Yocto is a highly versatile and flexible build system, capable of handling most use cases. The community is open, but it is also governed by the Yocto Project Advisory Board.

## Slide 16: Buildroot vs Yocto: Configuration
Buildroot reuses kconfig from the Linux kernel
  Entire configuration stored in a single .config/defconfig
  Defines all aspects of the system: architecture, kernel version/config, bootloaders, user-space packages, etc.
  Building the same system for different machines to be handled separately
In Yocto the configuration is separated in multiple parts:
  Distribution configuration (general configuration, toolchain selection, etc.)
  Machine configuration (defines the hw architecture, hw features, BSP)
  Image recipe (what system programs should be installed on the target)
  Local configuration (e.g., how many threads to use when compiling, whether to remove build artifacts, etc.)
  Allows to build the same image for different machines or using different distributions or different images for one machine
Notes: Next, is a comparison of Buildroot and Yocto in terms of configuration.
Buildroot reuses the “kconfig” functionality already provided by the Linux kernel. The entire configuration is stored in a single file called “.config/defconfig”. This file defines all aspects of the system, such as architecture, kernel version, bootloaders, user-space packages, etc. Building the same system for different machines is to be handled separately.
In Yocto, the configuration is split into multiple parts. There is distribution configuration, which handles the general configuration and toolchain selection. There is also machine configuration, which defines the hardware architecture, features, and the board support package (BSP). It also configures an image recipe, which will include details of which system programs should be installed on the target. Finally, there is the local configuration, which details how many threads to use when compiling, whether to remove build artifacts, and other information.
Yocto provides the ability to build the same image for different machines or distributions, or even a variety of images for one machine. This makes it a highly versatile and powerful tool.

## Slide 17: Buildroot vs Yocto: Purpose
Buildroot is intended for
  Very small root file systems (< 8 MB)
  Simple embedded system (with limited number of system programs)
  Non-dedicated build engineers (e.g., engineers that are not focused only in building embedded Linux)
Yocto is intended for
  Large root file systems
  Large embedded systems
  Support for multiple hw configurations
  Dedicated build engineers
public domain logo from yoctoproject.org
public domain image from Openclipart
Notes: Finally, we will compare the purpose of the two build systems.
Buildroot is typically intended for small root file systems, usually under 8 MB. It is generally used for simple embedded systems that only require a limited amount of system programs. It can be considered to be more geared towards use from non-dedicated build engineers. This means engineers that are not focused only on building embedded Linux systems.
Yocto is intended for larger root file systems and, in general, larger embedded systems. It provides support for multiple hardware configurations. It could be considered that Yocto is more geared towards dedicated build engineers that are primarily focused on working with embedded Linux systems.

## Slide 18: Summary
Introduction
The Workflow
The Build Systems
Yocto
Notes: We will now take a more in-depth look at Yocto and its workflow.

## Slide 19: The Yocto Project
Open-source project hosted by the Linux Foundation
Collaboration of multiple projects that make up the “Yocto Project”
  Bitbake: build tool
  OpenEmbedded core: software framework used for creating Linux distributions
  Poky: a reference distribution of the Yocto Project, containing the OpenEmbedded Build System (BitBake and OpenEmbedded Core) and a set of metadata to start building custom embedded Linux systems
  Application Development Toolkit: provides application developer a way to write sw running on the custom-built embedded Linux system without the need for knowing build systems
Support for Arm, MIPS, PPC, RISC-V, x86, and x86-64 architectures
Notes: The Yocto Project is an open source project that is hosted by the Linux Foundation. It brings together several related projects to offer an overall package called the “Yocto Project”.
Some of the individual projects are “Bitbake”, a build tool, and “OpenEmbedded Core”, a framework used for the creation of Linux distributions. Poky is also included in the project. Poky is a reference distribution of the Yocto Project, which contains the OpenEmbedded build system (Bitbake and OpenEmbedded Core) and a set of metadata to start building custom embedded Linux systems.
An Application Development Toolkit (ADT) is provided to enable application developers to write software to run on the custom-built embedded Linux system without knowing much about build systems.

## Slide 20: The Yocto Build System
It is composed of multiple layers which are containers for the building blocks of the system.
Layers do not contain components source code, only their metadata, called recipes.
Recipes define how to build binary outputs called packages.
Developer-specific layer
Commercial layer from operating system vendor
User interface-specific layer
Board Support Package layer
Yocto-specific layer metadata (meta-yocto)
OpenEmbedded core metadata (oe-core)
Notes: The Yocto build system is composed of multiple layers. These layers are essentially containers for the building blocks of the system. The layers do not contain component source code, but they do contain the metadata for them. These are called recipes. Recipes define how to build binary outputs, known as packages.

## Slide 21: The Build System Workflow
Source: http://www.yoctoproject.org/docs/2.1/mega-manual/mega-manual.html
Notes: This diagram illustrates the overall workflow of the Yocto build system. We will look at the individual parts in more detail.

## Slide 22: The Build System Workflow: Configuration Files
meta/conf/bitbake.conf – default configuration
build/conf/bblayers.conf – layers to be used during build process
*/conf/layers.conf – layer configuration
build/conf/local.conf – user-defined configuration
meta-yocto/conf/distro/poky.conf – distribution policy
meta-yocto-bsp/conf/machine/board-name.conf – configuration of the board support package
meta/conf/machine/include/tune-CPU-name.inc – CPU-specific configuration
User Configuration
Metadata (.bb + patches)
Machine (BSP) Configuration
Policy Configuration
Notes: For Yocto, the build system workflow has a number of different configuration files, for different purposes.
Meta/conf/bitbake.conf is where the default configuration settings are stored.
Build/conf/bblayers.conf is where the layers to be used during the build process are stored.
/conf/layers.conf is where the layer configuration settings are stored.
Build/conf/local.conf are where the user-defined configurations are stored.
Meta-yocto/conf/distro/poky.conf is where the distribution policy is stored.
Meta-yocto-bsp/conf/machine/board-name.conf is where the configuration settings for the BSP are stored.
Meta/conf/machine/include/tune/tune-CPU-name.inc is where the CPU-specific configuration settings are stored.

## Slide 23: The Build System Workflow: User Configuration
build/conf/local.conf is used to override the default configuration and define what to build.
  BB_NUMBER_THREADS and PARALLEL_MAKE
  MACHINE settings
  DISTRO settings
  INCOMPATIBLE_LICENSE = “GPLv3”
  EXTRA_IMAGE_FEATURES
build/conf/bblayers.conf is used to configure which layers to use.
  Add Yocto Project Compatible layers to the BBLAYERS
  Default: meta (oe-core), meta-yocto, and meta-yocto-bsp
Example for the Raspberry Pi 5
local.conf (fragment)
MACHINE ?= 'raspberrypi5'
DISTRO ?= 'poky'
bblayer.conf (fragment)
BBLAYERS = " \
${BSPDIR}/sources/poky/meta \
${BSPDIR}/sources/poky/meta-yocto \
${BSPDIR}/sources/poky/meta-yocto-bsp \
\
${BSPDIR}/sources/meta-openembedded/meta-oe \
${BSPDIR}/sources/meta-openembedded/meta-multimedia \
${BSPDIR}/sources/meta-openembedded/meta-networking \
${BSPDIR}/sources/meta-openembedded/meta-python \
\
${BSPDIR}/sources/meta-fsl-arm \
${BSPDIR}/sources/meta-fsl-arm-extra \
${BSPDIR}/sources/meta-fsl-demos \
${BSPDIR}/sources/meta-raspberrypi \
Notes: One part of the Yocto workflow involves user configuration. The “build/conf/local.conf” file is used to override the default configuration and to define what to build. Some settings include the following:
  “BB_NUMBER_THREADS”
  “PARALLEL_MAKE”
  “DISTRO”
  “INCOMPATIBLE_LICENSE = “GPLv3””
  “EXTRA_IMAGE_FEATURES”
The “build/conf/bblayers.conf” file is used to configure which layers to use. Yocto Project-compatible layers can be added to the “bblayers” file. The default layers are meta (o e core), meta-yocto, and meta-yocto-bsp.

## Slide 24: The Build System Workflow: Metadata
Recipes for building packages
Recipes inherit the system configuration and adjust it to describe how to build and package the software.
Can be extended and enhanced via layers
Compatible with OpenEmbedded
Example for the Raspberry Pi 5
rpi-basic-image.bb (fragment)
# Base this image on rpi-hwup-image
include rpi-hwup-image.bb
SPLASH = "psplash-raspberrypi"
IMAGE_FEATURES += "ssh-server-dropbear splash"
Notes: Another aspect of the Yocto workflow is metadata. Metadata can be thought of as the description of data. In Yocto, recipes are used for building packages. These recipes inherit the system configuration and adjust it to describe how to build and package the software. These can be extended and enhanced via layers. They are also compatible with OpenEmbedded.
Here is an example.

## Slide 25: The Build System Workflow: Machine (BSP) Configuration
Configuration files that describe a machine
  Define board specific kernel configuration
  Processor/SOC Tuning files
Machine configuration refers to kernel sources.
Compatible with OpenEmbedded
Example for the Raspberry Pi 5
raspberrypi5.conf (fragment)
#@TYPE: Machine
#@NAME: RaspberryPi 5 Development Board
#@DESCRIPTION: Machine configuration for the RaspberryPi 5
MACHINEOVERRIDES = "raspberrypi5:${MACHINE}"
MACHINE_EXTRA_RRECOMMENDS += " kernel-modules wl18xx-conf
uim-sysfs bt-firmware gator"
include conf/machine/raspberrypi5.conf
SERIAL_CONSOLE = "115200 ttyS0"
KERNEL_MODULE_AUTOLOAD += "g_serial hello"
MACHINE_ESSENTIAL_EXTRA_RRECOMMENDS += "kernel-module-gator"
Notes: Machine configuration is another stage in the workflow, and Yocto provides configuration files to describe a machine. They can define board-specific kernel configurations or process and system-on-chip tuning files.
The machine configuration refers to kernel sources.
As with other stages, this step is compatible with OpenEmbedded.
Here is an example of a machine configuration file.

## Slide 26: The Build System Workflow: Distribution Policy
Defines distribution policies that affect the way individual recipes are built
  May set alternative preferred versions of recipes
  May enable/disable features
  May configure specific package rules
  May adjust image deployment settings
Enabled via the DISTRO setting
Four predefined settings:
  poky-bleeding: enables bleeding edge packages
  poky: core distribution definition, defines the base
  poky-lsb: enable items required for Linux Standard Base support
  poky-tiny: construct a smaller than normal system
Notes: Distribution policies that affect the way individual recipes are built are defined in Yocto. These policies may:
  Set alternative preferred versions of recipes.
  Enable/disable features.
  Configure specific package rules.
  Adjust image deployment settings.
They are enabled via the DISTRO setting.
There are four predefined settings:
  Poky-bleeding, which enables bleeding edge packages
  Poky, which is the core distribution definition and defines the base
  Poky-lsb, which enables items required for Linux Standard Base (LSB) support
  Poky-tiny, which is for constructing a smaller-than-usual system

## Slide 27: The Build System Workflow: Source Fetching
Recipes tell the location of all sources, patches, and files.
  These may exist on the internet or be local (See SRC_URI in the *.bb files).
Bitbake can get the sources from git, svn, bzr, or tarballs.
Versions of packages can be fixed or updated automatically (Add SRCREV_pn-PN = "${AUTOREV}" to local.conf).
The Yocto Project mirrors sources to ensure source reliability.
Notes: Given that the project uses a variety of sources to build a certain target, the sources must be fetched. Recipes specify the location of all source, patches, and files. These may be stored locally or obtained via the Internet.
BitBake is able to get the sources from a variety of forms, such as Git, svn, bzr, and tarballs.
Differing versions of packages can be fixed or updated automatically by adjusting the “local.conf” file.
The Yocto Project mirrors the sources to ensure their reliability.

## Slide 28: The Build System Workflow: Patching
Once sources are obtained, they are extracted.
Patches are applied in the order they appear in SRC_URI.
In this stage, application-specific patches are applied.
  Custom modifications to the open-source code that are mandated by the specific application for which the embedded system is intended for
Notes: Once the sources are fetched, they are then extracted.
Next, patches are applied in the order that they appear in “source_uri”.
At this stage, the application-specific patches are applied. This includes customer modifications to the open-source code that are mandated by the specific application for which the embedded system is intended.

## Slide 29: The Build System Workflow: Configure/Compile/Install
The recipe specifies configuration and compilation rules.
  Various standard build rules are available, such as autotools and gettext.
  Standard ways to specify custom environment flags
  Install step runs under “sudo”, which allows special files, permissions, and owners/ groups to be set.
Notes: The recipe specifies the configuration and compilation rules. There are a variety of standard build rules that are available, such as “auto tools” and “get text”.
There are standard ways to specify custom environment flags.
The installation step runs under “sudo” and allows special files, permissions, and owners/groups to be set.

## Slide 30: The Build System Workflow: Output Analysis/Packaging
Output Analysis
  Categorize generated software (debug, dev, docs, and locales)
  Split runtime and debug information
Perform QA tests (sanity checks)
Package Generation
  Support the popular formats: RPM, Debian, and ipk
  Set preferred format using PACKAGE_CLASSES in local.conf
  Package files can be manually defined to override automatic settings.
Notes: In terms of output analysis, the generated software can be categorized, for example, debug, dev, docs, and locales. There is split runtime and debug information, too.
It performs quality assurance tests or “sanity checks” and then generates the packages. There is support for popular formats, such as RPM, Debian, and ipk. The preferred format can be set in the “local.conf” file.

## Slide 31: The Build System Workflow: Image Generation
Images are constructed using the packages built earlier and put into the Package Feeds.
Decisions of what to install on the image is based on the minimum defined set of required components in an image recipe. This minimum set is then expanded based on dependencies to produce a package solution.
Images may be generated in a variety of formats (tar.bz2, ext2, ext3, jffs, etc.).
Notes: When looking at image generation in regard to the overall workflow, images are constructed using the packages built earlier and put into the “package feeds”.
The decision of what to install on the image is based on the minimum required components in an image recipe. This minimum set is then expanded based on dependencies to produce a package solution.
Images can be generated in a variety of formats, such as “tar.bz2”, “ext2”, “ext3”, and “j f f s”.

## Slide 32: The Build System Workflow: SDK Generation
A specific SDK recipe may be created .
SDK may be based on the contents of the image generation.
SDK contains native applications, cross toolchain, and installation scripts.
May be used by the Eclipse Application Developer Tool to enable App Developers
Notes: Finally, software development kit (SDK) generation is the final step. A specific SDK may be created. This SDK might be based on the contents of the image generation. The SDK contains native applications, cross-compiling toolchain, and installation scripts.
It can be used by the Eclipse Application Developer Tool to enable App developers.
This concludes the fourth lecture on Linux for Embedded Systems. In the next module, we will take a look at Linux kernel modules.