## Slide 1: Embedded Linux
Linux-Based Embedded System Component Stack
Notes: Hello and welcome to the Linux for Embedded Systems lecture. This is the second lecture of the course.

## Slide 2: Goals
To illustrate the main components of a Linux-based embedded system
To analyze the bootstrap process
Notes: The aim of this lecture is to illustrate the main components of a Linux-based embedded system, as well as to look at the bootstrap process.

## Slide 3: Summary
Introduction
Bootloader
Kernel
Device Tree
System Programs
Application
Root Filesystem
Notes: We will start off by looking at some of the components that make up an embedded Linux system.

## Slide 4: Summary
Introduction
Bootloader
Kernel
Device Tree
System Programs
Application
Root Filesystem
Notes: We will start off by looking at some of the components that make up an embedded Linux system.

## Slide 5: Linux-Based Embedded System Components
Bootloader
  Software executed at power-up to set-up the hardware to run the operating system
Device tree
  A tree data structure with nodes that describe the physical devices in the hardware needed by the Linux kernel to initialize properly the device drivers
Linux Kernel
  The operating system code providing all the services to manage the hardware resources
Hardware
Application
System Programs
System Call Interface
Process Management
Virtual File System
Memory Management
Network Management
Device Drivers
Bootloader
Linux Kernel
Root File System
Device tree
Notes: A typical Linux-based embedded system is made up of numerous components. One of these components is the bootloader. This is a piece of software, executed at power-up to set up the hardware to run the operating system.
Another component is the device tree. This is a tree data structure with nodes that describe the physical devices in the hardware needed by the Linux kernel to initialize the device drivers.
Perhaps the most important component is the Linux kernel. This is essentially the operating system code and provides all the services to manage hardware resources and perform many other tasks.

## Slide 6: Linux-Based Embedded System Components
System Programs
  User-friendly utilities to access operating system services
Application
  Software implementing the functionalities to be delivered to the embedded system user
Root Filesystem
  Container for the Linux Kernel configuration files, the system programs, and the application
Hardware
Application
System Programs
System Call Interface
Process Management
Virtual File System
Memory Management
Network Management
Device Drivers
Bootloader
Device tree
Linux Kernel
Root File System
Notes: System programs are user-friendly utilities that implement and provide access to underlying operating system services.
Applications are software programs that implement the functionality required by the system to serve the user.
The root file system is the container of the Linux kernel configuration files, system programs, and the applications.

## Slide 7: Reference Hardware Model
Embedded System Hardware components:
  RAM: volatile memory storing data/code
  CPU: processor running software
  I/O: peripherals to get inputs from the user, and to provide outputs to the user
  Boot Flash: small non-volatile memory needed at power-up (discussed later)
  Mass Memory Flash: large non-volatile memory (discussed later)
CPU
Boot Flash
Mass Memory
Flash
I/O
RAM
Memory
Embedded System Hardware
Notes: In terms of hardware, embedded systems are made up of several components.
One component is the RAM (random-access memory), which is a type of volatile memory used for storing data and code that is currently in use.
Another component is the CPU (central processing unit), which is the processor that the software is run on. The CPU is where the computation occurs within the system and includes the arithmetic logic unit.
Embedded systems also include input/output (I/O) devices, which are peripherals that enable the communication of information between the system and the user.
They also include boot flash and mass memory flash. Boot flash is a smaller type of non-volatile memory and mass memory flash is large non-volatile memory storage. These will both be discussed later.

## Slide 8: Reference Hardware Model Implementations
Multiple implementations of the reference hardware model are possible. For example:
  Microcontroller-based implementation: a single device hosts most of the reference model components (e.g., CPU, RAM, boot flash).
  System-on-Chip implementation: most of the reference model components are discrete components, while the CPU is integrated with some of them (e.g., I/O, boot flash).
CPU
Boot Flash
I/O
RAM
Microcontroller (MCU)
Mass Memory
Flash
CPU
Boot Flash
I/O
RAM
System on Chip (SoC)
Notes: There are different ways in which the reference hardware model can be implemented. For example:
One option is a microcontroller-based implementation. This approach incorporates the majority of the reference model components onto a single device, typically including the CPU, RAM, boot flash, and I/O.
An alternative option is a system-on-chip (SoC) based implementation. In this approach, several of the reference model components are discrete. The CPU can then be integrated with some of them, for example, the I/O and boot flash.

## Slide 9: CPU Memory Map
The CPU generates 2N different addresses (02N-1).
  N=number of bits of the address bus
  a 32-bit address bus implies 2^32 (~4 billion ) addresses
Each device (e.g., memory, I/O) is associated with a range of addresses.
The memory map describes this association for all the devices.
Memory map of NXP LPC1768 (Cortex-M3)
Notes: When looking at a map of the CPU memory, you can see that different devices are allocated to different address ranges in memory. The CPU initially generates 2 to the power of n different addresses, where n is the number of bits of the address bus.
These addresses are then assigned to different devices or components (e.g., memory, I/O) that require space in memory.

## Slide 10: Summary
Introduction
Bootloader
Kernel
Device Tree
System Programs
Application
Root Filesystem
Notes: We will now look at the bootloader.

## Slide 11: The Role of the Bootloader
A processor is designed to run software from “somewhere”.
To start running the software, the processor needs to know:
  Where the software is located
  How to get access to the software location
  Where the stack is located
Notes: The bootloader plays an important role in the initial stages of the boot process. For software to run, the processor must know where the software is located, how it can access the location, and where the stack is located.

## Slide 12: The Role of the Bootloader
When powered-up, the processor needs a simple way to get the information it needs.
  Where the software is located
  How to get access to the software location
  Where the stack is located
At power-up, the program counter is set to a default known value, the reset vector.
  The software starting at the reset vector, which will load the bootloader, which takes care of providing the processor all the needed information.
  The operations performed depend on the system architecture.
Notes: When a system is powered-up, a program counter is set to a default known value, which is the reset vector. On Cortex-M, this is generally address 0x4
The program counter is a register that holds the address of the instruction that is next to be executed.
The reset vector is a pointer to an address that contains the first instruction to be executed for the firmware.
The bootloader is the first program to run and takes care of providing the processer with all the information it needs, such as startup software location, how to access it, and where the stack is located.
The specific operations performed in the bootloader are dependent on the system’s architecture.

## Slide 13: Possible Scenarios
Scenario 1, typical of microcontrollers
  All the software (bootloader + device tree + operating system + root filesystem) is stored in persistent storage (boot flash) embedded in the microcontroller.
  All the software is executed from the persistent storage.
  The CPU reset vector is located in the boot flash.
  The RAM is embedded in the microcontroller and is used for data, stack and heap only.
CPU
Boot Flash
I/O
RAM
Microcontroller (MCU)
Bootloader
Operating System
Application
System Programs
Data
Stack
Heap
Device tree
Root File System
Notes: Looking back at the two different implementations of the reference hardware model, we can see how the bootloader is used differently.
In the microcontroller-based implementation, all the software is stored in a form of persistent storage embedded within the microcontroller. This software is executed from the persistent storage.
The CPU reset vector, which points to the bootloader, is located in the boot flash.
Finally, the RAM is also embedded in the microcontroller and is used exclusively for data, the stack, and the heap.

## Slide 14: Possible Scenarios
Scenario 2, typical of System-on-Chip
  The bootloader is stored into the boot flash.
  The CPU reset vector is located in the boot flash.
  The root filesystem, operating system, and device tree are stored in the mass memory flash and loaded in RAM by the bootloader.
  The RAM is external to the SoC. It will store the operating system + application software, root filesystem (if configured as RAM disk), data, stack, and heap.
Mass Memory
Flash
CPU
Boot Flash
I/O
RAM
System-on-Chip
Bootloader
Operating System
Application
System Programs
Data
Stack
Heap
Device tree
Notes: In the system-on-chip (SoC) implementation of the reference hardware model, the arrangement is different.
The bootloader, along with the CPU reset vector, is still stored in the boot flash, similar to the microcontroller implementation.
However, unlike the microcontroller, the software components, such as applications, system programs, operating system, and device tree, are stored in the mass memory flash but are loaded into RAM by the bootloader.
Finally, the RAM is external to the system-on-chip and stores what has been loaded into it by the bootloader, as well as data, the stack, and the heap.

## Slide 15: An Example of Bootloader Operations
Let’s consider Scenario 2 for a given SoC with the following memory map:
  RAM 512 kbytes (arranged as 128 kwords, each 32 bits long), from 0x0002_0000 to 0x0003_FFFF
  Mass memory flash 256 kbytes (same organization as before), from 0x0001_0000 to 0x0001_FFFF
  Boot flash 256 kbytes (same organization as before), from 0x000_0000 to 0x0000_FFFF
Boot Flash
Mass Memory
Flash
RAM
0x0000_0000
0x0000_FFFF
0x0001_FFFF
0x0003_FFFF
CPU reset vector
Notes: Let’s look at an example of the bootloader’s operations for the system-on-chip (SoC) implementation.
The memory map for this scenario will look like this.
The RAM will be 512 kilobytes and will be assigned the addresses 0x0002_0000 to 0x0003_FFFF.
The mass memory flash will be 256 kilobytes and will be assigned the addresses 0x0001_0000 to 0x0001_FFFF.
Then finally, the boot flash will also be 256 kilobytes and will be assigned the addresses 0x000_0000 to 0x0000_FFFF.

## Slide 16: An Example of Bootloader Operations
Time = before power up
The boot flash is preloaded with the bootloader
  First bootloader instruction at 0x0000_0FFF
  Last bootloader instruction at 0x0000_AFFF
The mass memory flash is preloaded with:
  Device tree (DT)
  Operating systems (OS)
  System programs (SP)
  Application
Boot Flash
Mass Memory
Flash
RAM
0x0000_0000
0x0000_FFFF
0x0001_FFFF
0x0003_FFFF
CPU reset vector
Bootloader
b 0x0000_0FFF
OS
Application
SP
0x0000_0000
0x0000_AFFF
DT
Notes: This is the state of the memory map before power up.
The boot flash address range is preloaded with the bootloader. In this diagram, the first bootloader instruction will be positioned at 0x0000_0FFF while the final instruction will be at 0x0000_AFFF.
The mass memory flash address range is preloaded with the components such as the device tree, the operating system, the systems programs, and the applications.

## Slide 17: An Example of Bootloader Operations
Time = power up
The CPU starts executing software from the reset vector:
  It jumps to the first instruction of the bootloader.
  It runs the bootloader software from boot flash memory.
Boot Flash
Mass Memory
Flash
RAM
0x0000_0000
0x0000_FFFF
0x0001_FFFF
0x0003_FFFF
CPU reset vector
Bootloader
b 0x0000_0FFF
0x0000_0000
0x0000_AFFF
OS
Application
SP
DT
Notes: This is the state of the memory map during power up.
At this point, the CPU starts executing processes using the reset vector. It will initially jump to the first instruction of the bootloader and then run the bootloader software from boot flash memory.

## Slide 18: An Example of Bootloader Operations
Time = during bootstrap
The CPU executes bootloader software that:
  Initializes the CPU RAM controller
  Sets up the CPU registers for mapping stack and heap to RAM
  Copies device tree, operating system, system programs, and applications to RAM
Boot Flash
Mass Memory
Flash
RAM
0x0000_0000
0x0000_FFFF
0x0001_FFFF
0x0003_FFFF
CPU reset vector
Bootloader
b 0x0000_0FFF
0x0000_0000
0x0000_AFFF
OS
Application
SP
DT
Notes: The next state is during the bootstrap process. In this phase, the CPU's RAM controller will be initialized, and the CPU registers for mapping the stack and heap to RAM will be set up.
Finally, the device tree, operating system, system programs, and applications are copied to RAM.

## Slide 19: An Example of Bootloader Operations
Time = end of bootstrap
The bootloader jumps to the first instruction of the operating system.
The CPU now executes the operating system software, which is responsible for:
  Setting up the execution environment for the application
  Starting application execution
Boot Flash
Mass Memory
Flash
RAM
0x0000_0000
0x0000_FFFF
0x0001_FFFF
0x0003_FFFF
CPU reset vector
Bootloader
b 0x0000_0FFF
0x0000_0000
0x0000_AFFF
Stack
Heap
OS
Application
SP
DT
OS
Application
SP
DT
Notes: The final stage we will look at is the end of the bootstrap, during which the bootloader jumps to the first instruction of the operating system.
The CPU then executes the operating system software, which is responsible for setting up the execution environment for applications and the starting application execution.

## Slide 20: Summary
Introduction
Bootloader
Kernel
Device Tree
System Programs
Application
Root Filesystem
Notes: Next, we will take a look at the Linux kernel.

## Slide 21: Linux Kernel
The Linux Kernel is the software responsible for optimally managing the embedded system’s hardware resources.
It offers services such as:
  Process management
  Process scheduling
  Inter-process communication
  Memory management
  I/O management (device drivers)
  File system
  Networking
  And more
System Call Interface
Process Management
Virtual File System
Memory Management
Network Management
Device Drivers
Linux Kernel
Notes: The Linux kernel is the software, or operating system kernel, responsible for optimally managing the embedded system’s hardware resources.
It offers a range of services that perform essential operating system functions. These include process management and scheduling through mechanisms such as task schedulers. This is primarily to do with how the CPU allocates its resources to different processes that require execution concurrently, and how they are scheduled to prevent any conflicts or interrupts within the system.
The kernel also enables processes to communicate and share data through inter-process communication. This can be achieved in a variety of ways. One method is via sockets, which send data via a network interface to another process. Another method is shared memory, where multiple processes have access to the same block of memory. The processes can then alter this block and share information.
Memory and I/O management are also included. We briefly looked at memory management in earlier slides, at how devices are allotted address ranges in memory. I/O management is supported via device drivers, allowing the user to control or interact with external devices that are attached to the system.
There is also support for a range of file system types that detail the structure of how information is stored, laid out, and accessed on the system.
Additionally, there is support for network management such as network protocols and network device drivers. Users have the ability to configure network settings and enable them to interact with networks.

## Slide 22: Linux Kernel
The Linux kernel adopts a layered operating system architecture:
  The operating system is divided into two layers, one (User space) built on top of the other (Kernel space).
  User space and Kernel space are different regions of the memory address space.
  Basic services are delivered by a single executable, monolithic Kernel.
  Services can be extended at run-time through loadable Kernel modules
Application
System Programs
System Call Interface
Process Management
Virtual File System
Memory Management
Network Management
Device Drivers
Kernel Space
User Space
Loadable Module
Monolithic kernel
Notes: The Linux kernel follows a layered operating system architecture. This leads to the operating system being divided into two main layers. One layer is user space; this layer is typically the higher-level parts of the system and mainly consists of applications or system programs, essentially, code that does not run on the operating system’s kernel. This is built on top of the kernel space layer. This is where the kernel operates, executing services for the system. These two layers occupy separate regions of the address spaces.
Basic services are delivered by one single executable. This is in line with monolithic kernels, where the entire operating system works in kernel space.
These services can be extended or added to at run-time by using loadable kernel modules (LKMs).

## Slide 23: Linux Kernel
Application
System Programs
System Call Interface
Process Management
Virtual File System
Memory Management
Network Management
Device Drivers
Kernel Space
User Space
Loadable Module
Monolithic kernel
Advantage
  Good separation between application/system programs and kernel. Bugs in the user space do not corrupt the kernel.
Disadvantages
  Bugs in one kernel component (for example, a new device driver) can crash the whole system, generally with a kernel panic
Notes: One advantage to the Linux kernel layout is it provides good separation between applications or system programs and the kernel. This means that any bugs that occur in user space will not affect or corrupt the kernel.
However, a disadvantage is that if there is a bug in one kernel component, such as a new device driver, it has the potential to crash the entire system (usually with a kernel panic event which halts the running system)

## Slide 24: Summary
Introduction
Bootloader
Kernel
Device Tree
System Programs
Application
Root Filesystem
Notes: We will now take a quick look at the device tree.

## Slide 25: Device Tree
To manage hardware resources, the Kernel must know which resources are available in the embedded system (i.e., the hardware description: I/O devices, memory, etc.).
There are two ways to provide this information to the Kernel:
  Hardcode it into the Kernel binary code. Each modification to the hardware definition requires recompiling the source code.
  Provide it to the Kernel when the bootloader uses a binary file, the device tree blob.
A device tree blob (DTB) file is produced from a device tree source (DTS).
  A hardware definition can be changed more easily as only DTS recompilation is needed.
  Kernel recompilation is not needed upon changes to the hardware definition. This is a big time saver.
Notes: For the kernel to manage hardware resources, it needs to know which resources are currently available in the embedded system (i.e., the hardware description, such as I/O devices, memory, and others).
This information can be provided to the kernel in two ways. One method is to hardcode it into the kernel binary code. However, this means that each modification to the hardware definition would require the source code to be recompiled. The alternative is to provide it to the kernel when the bootloader uses a binary file, which is known as the device tree blob (DTB).
A device tree blob is a file that is produced from a device tree source (DTS). Hardware definitions can be changed more easily, as only the device tree source needs recompilation, saving time by not needing to recompile the kernel.

## Slide 26: Summary
Introduction
Bootloader
Device Tree
Kernel
System Programs
Application
Root Filesystem
Notes: Next, we shall look at system programs.

## Slide 27: System Programs
System programs provide a convenient environment for program development and execution.
They can be divided into:
  Status information (e.g., uptime)
  File modification (e.g., mv)
  Programming language support (e.g., gcc)
  Program loading and execution (e.g., ld)
  Communications (e.g., ping)
  Application programs (e.g., firefox)
Notes: System programs are executable from the command line and provide a convenient environment for program development and execution.
They can be divided into the following:
- Status information
- File modification
- Programming language support
- Program loading execution
- Communications
- Application programs
Some examples are ls, cd, cat, and chmod.

## Slide 28: Summary
Introduction
Bootloader
Device Tree
Kernel
System Programs
Application
Root Filesystem
Notes: Next, we will look at applications.

## Slide 29: Application
The application is the software required to provide the end user with service for which the embedded system was conceived.
Examples can be found in many different products:
  Network Attached Storage (NAS)
  Network router
  In-vehicle infotainment
  Specialized lab equipment
  And more
Notes: An application is the software required in order to provide the user with a service, typically the primary purpose or which the embedded system was designed.
There are a variety of examples that can be found in products, such as
  - Network-attached storage (NAS)
  - Network router
  - In-vehicle infotainment
  - Specialized lab equipment

## Slide 30: Summary
Introduction
Bootloader
Device Tree
Kernel
System Programs
Application
Root Filesystem
Notes: Finally, we will take a quick look at the root file system.

## Slide 31: Root Filesystem
The Linux Kernel needs a file system, called a root filesystem, at startup.
  It contains the configuration files needed to prepare the execution environment for the application (e.g., setting up the Ethernet address).
  It contains the first user-level process (init).
The root filesystem can be:
  A portion of the RAM treated as a file system known as Initial RAM Disk (initrd), if the embedded system does not need to store data persistently during its operations.
  A persistent storage in the embedded system, if the embedded system has to store data persistently during its operations.
  A persistent storage accessed over the network, if developing a Linux-based embedded system.
Notes: Upon startup, the Linux kernel requires a file system, known as the root file system. This contains all the configuration files that are required in order to prepare the execution environment for the application, for example, setting up the Ethernet address.
It also contains the first user-level process: init.
A root file system can be:
  A portion of RAM that is treated as a file system. This is known as an “initial RAM disk” or “initrd”. This can be used if the embedded system does not need to store data persistently during its operations.
  A persistent storage in the embedded system, if the embedded system has to store data persistently during its operations
  A persistent storage accessed over the network, if developing a Linux-based embedded system

## Slide 32: Typical Layout of the Root Filesystem
/ # Disk root
/bin # Repository for binary files
/lib # Repository for library files
/dev # Repository for device files
console c 5 1 # Console device file
null c 1 3 # Null device file
zero c 1 5 # All-zero device file
tty c 5 0 # Serial console device file
tty0 c 4 0 # Serial terminal device file
tty1 c 4 1 #
tty2 c 4 2 #
tty3 c 4 3 #
tty4 c 4 4 #
tty5 c 4 5 #
/etc # Repository for config files
inittab # The inittab
/init.d # Repository for init config files
rcS # The script run at sysinit
/proc # The /proc file system
/sbin # Repository for accessory binary files
/tmp # Repository for temporary files
/var # Repository for optional config files
/usr # Repository for user files
/sys # Repository for system service files
/media # Mount point for removable storage
Folder icons by Icons8
Notes: Here is an example of what you might expect to see in a typical root file system.
This concludes the second lecture on Linux for Embedded Systems. In the next module, we will look at the Linux architecture and the bootloader.